## Slide 1
FINAL PRESENTATION · 2026.06.22
HADO Smart Court IoT
Real-time player tracking, tactical guidance, and 17-keypoint action recognition on Raspberry Pi 4
Jinwoo Park
Team lead · HADO Smart Court IoT

## Slide 2
01 · PROBLEM
The game is real-time. The analysis is not.
HADO is an AR sport played 3 vs 3 on a 10 × 6 m indoor court.
Coaches review footage after a match — by then the moment is gone.
Our question:
Can we deliver tactical feedback as it happens, with just a single camera and a Raspberry Pi?
10 × 6 m
COURT · INDOOR AR ARENA
3 vs 3
PLAYERS · HEADSET-WORN AR
< 200 ms
TARGET FEEDBACK LATENCY
HADO Smart Court IoT · Final Presentation · Jinwoo Park
2 / 13

## Slide 3
02 · SYSTEM
Single camera → Pi 4 → three-level inference stack
Camera
USB / HDMI capture
Capture
src/camera.py
Detector
YOLOv8n-pose
Tracker
IoU + ID
Homography
px → court m
Outputs
see below
L1
Bird-eye tracking
Live player positions on a 10×6 m court map.
L2
Tactical engine
Six rules (R1–R6) → arrow + voice guidance.
L3
Action recognition
17 keypoints → 7 actions → next-action recommendation.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
3 / 13

## Slide 4
03 · HARDWARE
Edge hardware: $80 of components, fully offline
Raspberry Pi 4 Model B
SPECIFICATION
Quad-core Cortex-A72 @ 1.5 GHz · 8 GB RAM
USB 3.0 × 2 · CSI camera port · Gigabit LAN
ROLE
Edge compute · Pose inference · Logging
Camera
SPECIFICATION
Arducam IMX519 16 MP CSI / GoPro · Sony via
HDMI → USB 3.0 capture board (UVC, 1080p60)
ROLE
Single-view court capture
Output
SPECIFICATION
HDMI display for on-court HUD
pyttsx3 offline TTS (Korean voice)
ROLE
Real-time visual + voice feedback
Fully offline. No cloud, no internet during operation. All inference, logging, and feedback happen on the Pi.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
4 / 13

## Slide 5
L1
TRACKING
Where is each player, frame by frame?
1
YOLOv8n-pose @ 320 × 320
Bounding box + 17 keypoints per player, single forward pass.
2
IoU tracker
Persistent ID across frames; track buffer 60 frames.
3
Foot-point homography
Bottom-center of bbox is always on the ground plane → geometrically correct meter coords.
4
Bird-eye renderer
Live 10 × 6 m court map.
INFERENCE THROUGHPUT
Mac (development)
98 FPS
Raspberry Pi 4 (NCNN, FP16)
≥ 15 FPS · target
Why this matters
15 FPS is the minimum latency floor for tactical relevance — anything slower and the recommendation lags the action.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
5 / 13

## Slide 6
L2
TACTICAL ENGINE
Six rules. One urgency arrow per player.
R1
MID
Spacing
Maintain ≥ 1.5 m from teammates
R2
MID
Lane cover
Cover open lanes toward goal
R3
HIGH
Counter threat
Block fast-approaching opponent
R4
MID
Gap attack
Exploit unguarded opponent zones
R5
HIGH
Backline defense
Keep one player near goal area
R6
MID
Formation
Maintain triangle / staggered shape
WHY RULES, NOT ML?
Interpretability — every arrow ships with the rule that fired it. No labeled data — this rule engine is the data collection tool for future ML work.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
6 / 13

## Slide 7
L3
ACTION RECOGNITION
17 keypoints → what the player is doing — at any camera distance.
17 COCO KEYPOINTS
nose · shoulders · elbows · wrists · hips · knees · ankles
7 HADO-SPECIFIC ACTIONS
↑
charge
wrist above shoulder, near-vertical
⚡
shoot
wrist extended toward opponent side
🛡
shield
both wrists wide, above elbows
←
dodge_l
shoulder midpoint left of hip midpoint
→
dodge_r
shoulder midpoint right of hip midpoint
↓
crouch
shoulder–knee vertical compression
●
ready
default (no other rule fires)
CAMERA-DISTANCE INVARIANCE
scale = max(shoulder_width, torso_height × 0.6, 30 px)
All action thresholds divide by this scale, so the same logic works at 2 m or 5 m.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
7 / 13

## Slide 8
L3
NEXT ACTION RECOMMENDATION · NEW
Not just what you ARE doing — what to do NEXT.
TRANSITION TABLE · NEXT_ACTION_RECS
current | next | reason | priority
charge | shoot | 차지 완료 → 발사 | 1.0
charge | dodge_l | 발사 포기 → 좌측 회피 | 0.3
shoot | dodge_r | 발사 후 우측 회피 | 0.8
shoot | dodge_l | 발사 후 좌측 회피 | 0.7
shield | charge | 방어 해제 → 역공 차지 | 0.9
dodge_l | charge | 회피 후 역공 차지 | 0.8
ready | charge | 차지 시작 | 0.7
RECOMMENDATION LOGIC
recommend_next_action(current, history)
1.
Look up base recommendations for current action.
2.
If same action persisted ≥ 4 frames, boost transition priority ×1.2.
3.
Sort by priority, return top 2.
Result on screen: two recommended next actions with reasons and color-coded icons in the bottom HUD panel.
From WHERE to WHAT NEXT. Court position → individual action → tactical next step. One pipeline, three layers of feedback.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
8 / 13

## Slide 9
04 · EDGE OPTIMIZATION
Three optimizations to hit 15 FPS on a $35 CPU
NCNN model format
≈ 3 ×
vs. ONNX on Pi 4
ARM-optimized FP16. Native to the Pi CPU — no PyTorch, no TensorRT.
Threaded capture
0 ms
camera wait time
Background thread holds the latest frame. Inference loop never blocks on V4L2 read.
imgsz = 320
− 75 %
pixels vs. 640×640
Single biggest FPS win. 320 is still above the YOLOv8n receptive-field floor for adult bodies.
Combined effect: the full Level 1 + 3 pipeline (detector + tracker + action classifier) runs end-to-end on Pi 4 CPU only.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
9 / 13

## Slide 10
05 · VALIDATION
272 unit tests, on-court measurements, rule-level coverage
272
UNIT TESTS PASSING
15
CORE MODULES COVERED
7
ACTION-CLASS TEST SETS
≤ 10 cm
POSITION ERROR TARGET
PI 4 FIELD MEASUREMENTS · W5
metric | target | Pi 4 measured | status
NCNN inference FPS | ≥ 15 fps | [TODO] | pending
ONNX inference FPS | ≥ 10 fps | [TODO] | pending
RAM usage | < 1.5 GB | [TODO] | pending
CPU temperature (30 min) | < 70 °C | [TODO] | pending
TTS guidance latency | < 500 ms | [TODO] | pending
[TODO] slots will be populated from this week's on-court session.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
10 / 13

## Slide 11
06 · LIVE DEMO
See the three levels working together.
▶
data/demo_track_a_pivot.mp4
RUN COMMANDS
Level 1 + 2
python -m src.main
--level 2 --voice
Level 3
python -m src.action_demo
--source 1 --show-kp-ids
Pi 4 (NCNN)
./run.sh action_live
--show-kp-ids
HADO Smart Court IoT · Final Presentation · Jinwoo Park
11 / 13

## Slide 12
07 · RESULTS
What we built — and what comes next
DELIVERED
✓
Fully offline, single-camera tactical analysis system
✓
Level 1 tracking — YOLOv8n-pose + IoU tracker + homography
✓
Level 2 tactical engine — six interpretable rules, voice guidance
✓
Level 3 action recognition — 7 actions with scale-normalized classifier
✓
Next-action recommendation — transition table + history weighting
✓
Pi 4 NCNN optimization — threaded capture + imgsz 320
✓
272 unit tests covering all core modules
FUTURE WORK
1
Auto-tune rule thresholds
Use 635 expert-annotated movement records to fit R1–R6 weights instead of hand-coding.
2
Replace transition table with sequence model
LSTM / small transformer over 30-frame action histories.
3
Multi-camera occlusion handling
Two-camera Bayesian fusion when players overlap.
4
AR effect overlay tolerance
Robustness when HADO virtual projectiles cover the player's body.
HADO Smart Court IoT · Final Presentation · Jinwoo Park
12 / 13

## Slide 13
Thank you.
Questions?
Jinwoo Park
github.com/jinwoo04/HADO_SMART_COURT_IOT
HADO Smart Court IoT · Final Presentation · 2026.06.22